SLIP package	Page 1	March 1, 1993


What is SLIP?	1
How Does It Work?	1
What is the SLIP package?	3
SLIP.BAT	3
UMSLIP.COM	3
TERMIN.COM	3
PHONE.EXE	3
Documentation	3
SLIPDISK	3
Where to Get It	4
SLIP.BAT	4
SETUP	4
POPMAIL	4
GOPHER	5
TELNET	5
FTP	5
QUIT	5
UMSLIP.COM	5
TERMIN.COM	5
PHONE.EXE	6
The HELP system (F1 Key)	6
Hot Keys	6
Cross-References (Hypertext)	7
Mouse	7
Previous Key (Alt-F1)	7
Index	7
Contents	7
Help-with-Help	7
The Primary Screen	8
The Menu Bar	8
Selecting from the Menu Bar	8
The System (Alt-Space)	9
Actions (Alt-A)	9
Setup (Alt-S)	10
Server Window	19
Time Display	20
The Lower Status Bar	20
Active Keys display	20
Context-Sensitive display	20
Transaction Log Window	20
Command-line operations	20
PHONE DIAL	21
PHONE HANGUP	21
PHONE FORCE <command>	21
PHONE WRITE	21
PHONE ?	21
Scripts	21
Built-in scripts	22
How to make custom scripts	22
PHONE WRITE	22
PHONE.CMD	22
The SLIPScript Language	23
SLIPScript Elements	23
SLIPScript commands	23
Writing a script	30
Debugging a script	30
Let us know about your scripts.	31

What is SLIP?

SLIP stands for Serial Line Internet Protocol, and is a way to 
establish a network connection through a modem.  What this means 
is that programs like POPMail, Gopher and NCSA Telnet will operate 
over telephone lines and through your modem, as if connected to the 
network by a network card.

Normal network connections are usually very fast (on the order of 10 
million bits per second, as compared with 10 thousand bits per 
second with the fastest modem), so applications running over a SLIP 
connection may seem to run somewhat more slowly than they would 
on a hardwired network connection.  

However, there are many advantages to using networked 
applications rather than standard modem communication programs 
such as Procomm.  For one, you can take advantage of client-server 
protocols such as Gopher or POP, which allow your computer to do 
some of the computing work, and to store the files received on your 
hard drive rather than on a remote host computer.  Another 
advantage is the ability to run multiple sessions:  programs like NCSA 
Telnet will allow you to connect to multiple hosts at one time, and to 
transfer files in the background while working in another window.

In order for this to work, your local network must have a "SLIP 
server".  A SLIP server is a computer which monitors incoming 
modems for SLIP connections and translates the modem signals into 
standard TCP/IP network signals.  You may also have some form of 
security system controlling who can connect to a SLIP server and 
receive an IP address.  You should check with your local network 
administrator to see if SLIP is available.

How Does It Work?

Developers of network applications often design their software to use 
the Packet Driver Specification.  A packet driver is a small piece of 
software that handles communications between your computer and 
the outside world.  A packet driver communicates with an ethernet 
board, a Token Ring card, a serial communications port, or some 
other piece of hardware that is connected to the network.  It 
provides the "glue" that allows the network application to 
communicate properly with the network.  Applications written to the 
Packet Driver Specification do not need to know how to communicate 
with ever possible network adapter; they just need tonow how to 
address the packet driver.  Figure 1 shows how this works.

                                           

Figure 1.  How network packet drivers work.


The UMSLIP packet driver is written specially for SLIP 
communications, and uses your serial port instead of a network 
adapter card to make a network connection.


                                        

Figure 2.  How UMSLIP makes a network connection


Network applications such as POPMail and Gopher talk only to the 
packet driver interface to get their information.  The UMSLIP packet 
driver replaces the packet driver normally used with a network 
adapter card, and  sends the data out the serial port of your 
computer instead (Figure 2).  The network application can't tell the 
difference:  it's only talking to the interface.  So all your network 
applications function as if they are physically connected to the 
network.

What is the SLIP package?

Everything that's necessary to make a SLIP connection can be found 
together in the SLIP.ZIP compressed file.  These include:

SLIP.BAT

A convenient batch file which makes it easy to use all of the network 
applications with SLIP.

UMSLIP.COM

The SLIP packet driver which translates program network signals 
into modem signals.

TERMIN.COM

The unaltered NCSA TERMIN.COM program for removing 
UMSLIP.COM from memory.

PHONE.EXE

The program which dials the telephone and establishes a SLIP 
connection.

Documentation

PHONE.DOC is this file

PHONE.HLP is the on-line help database for PHONE.EXE

README.TXT is the help file for SLIP.BAT.

UMSLIP.DOC is a help file for UMSLIP.COM.

SLIPDISK

As a supplement to the basic SLIP package contained in SLIP.ZIP, an 
automatic installation package is available called SLIPDISK.ZIP.  It 
contains the PHONE, POPMAIL, GOPHER, and NCSA Telnet and FTP 
programs, plus the installation program.

Where to Get It

SLIP.ZIP and SLIPDISK.ZIP are available via anonymous FTP from 
boombox.micro.umn.edu in the /pub/slip directory.  SLIPDISK.ZIP is 
in the slipdisk subdirectory, and is easiest to use when unzipped onto 
a 1.44Meg 3 1/2" disk labelled DISK1.  To do so, type the command

	PKUNZIP -D SLIPDISK.ZIP A:

SLIP.BAT

SLIP.BAT is a batch file that automates SLIP.  Simply type "SLIP 
XXXXX" to run option XXXXX via a SLIP connection.

The SLIP batch file will:

1) Check to see if the UMSLIP packet driver is loaded, and loads it if 
necessary.

2) Check to see if there already is a SLIP connection and creates one 
only if necessary.

3) Run the program requested if everything is correct.

SLIP SETUP

Before you can successfully establish a SLIP connection, you need to 
set up both your Modem parameters (Baud Rate, Word Length, etc.) 
and your SLIP parameters (Username, Password, etc.)  The command 
SLIP SETUP will automatically run the PHONE program and present 
the configuration screens for easy access.

SLIP POPMAIL

Establishes the SLIP connection if necessary, then runs POPMAIL.

SLIP GOPHER

Establishes the SLIP connection if necessary, then runs GOPHER.

SLIP TELNET <parameters>

Establishes the SLIP connection if necessary, then runs TELNET.  For 
example:

	SLIP TELNET LUMINA.LIB.UMN.EDU

SLIP FTP <parameters>

Establishes the SLIP connection if necessary, then runs FTP.  For 
example:

	SLIP FTP BOOMBOX.MICRO.UMN.EDU

SLIP QUIT

If you are all done using slip and want to free up about 6k of 
memory, you can type "SLIP QUIT".  This disconnects your modem, 
and then unloads the UMSLIP.COM packet driver from memory.

UMSLIP.COM

The PHONE program needs the UMSLIP packet driver in order to talk 
to the modem.  If you use the SLIP.BAT batch file, it will 
automatically run UMSLIP for you.

If you want, you can run UMSLIP from your AUTOEXEC.BAT file to 
ensure that it is always ready.

UMSLIP uses about 6k of RAM.

TERMIN.COM

TERMIN.COM will remove the UMSLIP.COM packet driver from 
memory.  See SLIP QUIT above.

PHONE.EXE

PHONE establishes a connection to the SLIP server or terminates an 
active connection.  It does this by sending commands to your modem 
to dial the phone, and then sending your login information to 
validate the connection with the SLIP server.  The UMSLIP.COM 
program must be run before PHONE.EXE.

The HELP system (F1 Key)

To access PHONE's Help System, press the F1 key.  A window will
open containing information about the menu item or dialog box field 
that is currently in the foreground.  This is known as "context-
sensitive" help.

You can browse through the help text using the

	Description	Key
	up arrow		­
	down arrow 	¯
	Page Up		PgUp
	Page Down		PgDn

keys on the keypad.

When you are finished using the help, press the Escape (Esc) key.

Hot Keys

Some menu commands are considered to be so important that they 
need to be available with a quick keypress short-cut:  a "hot key" 
that goes straight to that command.  Hot keys for PHONE are shown 
below.

	Hot-Key	Command
	F1		Help
	F2		Dial
	F3		Hang up
	F5		Exit
	Alt-X	Exit

Cross-References (Hypertext)

Some help messages contain Cross-References to other topics.   Cross-
References are displayed in a different color from normal help text.  
One cross-reference is always highlighted.  If you press Enter, the 
help message associated with the cross-reference is displayed.  If 
there are several cross-references within a help message, you can 
press the Tab or Shift-Tab keys to move the highlight to the next or 
previous cross-reference.


Mouse

If your computer has a mouse, move the cursor over a cross-
reference and click the left mouse button twice to select it.  Double 
Clicking (pressing the left mouse button twice in rapid succession) 
has the same effect as pressing the Enter key.

Previous Key (Alt-F1)

Press the PREVIOUS button (Alt-F1) to "back up" one page to the 
previously-selected HELP topic.

Index

An alphabetical listing of every on-line help entry.

Contents

Help entries organized by subject and category.

Help-with-Help

You can use PHONE's on-line Help from the Help menu or via hot 
keys.

Wherever you are in PHONE, you can press F1 to see a help
screen about the menu command or dialog-box item that's 
currently active.


To learn more about using on-line Help, use the arrow keys
to move the cursor to one of the Help keywords; then press ENTER.

You can also press TAB to jump to the next Help keyword,  and then 
press ENTER.

If you're using a mouse, just click the Help keyword you're 
interested in.

The Primary Screen

The Primary Phone Screen consists of four parts:  a top Menu Bar, a 
message space below, a Transaction Log window where the progress 
of the connection can be observed, and a lower Status Bar.

The Menu Bar

The Menu Bar consists of the primary groups of PHONE commands 
available on pull-down menus.  You can open these menus by 
selecting a given Menu Bar item with the mouse (by positioning the 
cursor over a given item and clicking the left button), or by pressing 
keys for those who don't use a mouse.

Selecting from the Menu Bar

There are three ways to select a menu command:

 F10

Press F10, then use the left and right arrow keys to select the 
appropriate menu and use the the up and down arrow keys to select 
a command.  Press Enter to choose the selected command.

Alt

Press Alt and the highlighted letter of the menu you want (such as 
Alt-F for the File menu), use the up and down arrow keys to select a 
command, then press Enter to choose that command.

You can also press the highlighted letter of a menu name or 
command instead of using the arrow keys.

Mouse

Click on the title of the menu you want to pull down, then click on 
the menu command you want to choose.

The highlighted menu title is the currently selected menu.

Menu commands are followed by an ellipsis (...), an arrow, or a hot 
key.  An ellipsis indicates that selecting that option will bring up a 
dialog box, as opposed to immediately initiating a program action.

The System (Alt-Space)

The System appears on the far left of the menu bar and is 
represented by the = symbol.  Alt-Spacebar is a keyboard shortcut 
that you can use at any time to pull down this menu.

The = menu contains the "About" item.  Some other programs will 
provide some utilities under this menu.

About

When you choose the About command from the System menu, a 
dialog box appears, showing copyright and version information.

Press ESC, click OK, or click Cancel to close the box.

Actions (Alt-A)

Phone can either Dial (F2) to establish a SLIP connection, or
Hang Up (F3) to break the connection and clear the phone line.  
Finally, you can Exit (Alt-X) from the program.

Dial (F2)

Once you have used the Setup options to configure your modem and 
to enter  your user name and password, the DIAL command will 
place the call and establishing the SLIP connection.

You can watch the lower Transaction Log window to observe the 
progress of the connection.

After you have configured the DIAL menu, you can also type the 
command PHONE DIAL from DOS.  This will run PHONE and attempt 
to establish the SLIP connection with no further commands on your 
part.

If the program fails to establish the connection for some reason, it 
will return an ERROR CODE, id used in DOS batch files (such as the 
SLIP.BAT file, see above) to decide whether to proceed to the next 
command in a batch file.

You can begin dialing by using the mouse to click on Actions:Dial,  by 
typing Alt-A then D, or by pressing the F2 key.

Hangup (F3)

If your modem is already connected to a SLIP server or any other 
service, HANGUP will disconnect it and hang up the phone.  You can 
also do this by typing the command PHONE HANGUP from DOS.

You can hang up by using the mouse to click on Actions:Hangup, by 
typing Alt-A and then H, or by pressing the F3 key.

Quit (Alt-X)

Use the Exit command when you are done using PHONE.

Note that this does not hang up the phone or break your SLIP 
connection (see the Actions:Hangup command).  It simply quits from 
the PHONE.EXE program.

You can quit PHONE by using the mouse to click on Actions:Exit, by 
typing Alt-A and then X, or by typing Alt-X.

Setup (Alt-S)

Before you can establish a SLIP connection, you need to configure 
both your Modem parameters (F4) (Baud Rate, Word Length, etc.) 
and your SLIP parameters (F5) (Username, Password, etc.)

Modem (F4)

The settings in this dialog box are used to tell your computer how to 
talk to your modem.  The speed of the modem, where it's connected, 
and what kind of modem it is are among the characteristics which 
need to be set so that your computer and modem can communicate.

While this window may look complex, you should need to set only a 
few of the options.  You will need to select the Baud Rate, Com Port, 
and Modem List entries will need to be set, but the Advanced entries 
are likely to be fine the way they are.


Baud Rate

The Baud Rate is the speed at which modems and computers talk to 
each other.

If your modem does not feature data compression, click on the 
highest baud rate at which your modem can communicate.  If your 
modem does feature data compression, click on a rate 2 to 4 times 
higher than the highest baud rate at which your modem can 
communicate.  Examples:

If you have a Hayes (TM) SmartModem 1200, a modem that does not 
do data compression, click on 1200.

If you have a Multi-Tech (TM) MultiModem II, which is a 9600 baud 
modem with data compression, click on 19,200 or 38,400.

If you choose a baud rate higher than that at which your modem can 
communicate, you'll also have to check the boxes labeled CTS and RTS
Handshaking (see below).  This prevents your modem from 
overwhelming your computer with data.

Data Errors

Your modem may be able to detect transmission errors (caused by 
static on the line, for instance) and correct them.  It corrects the 
error by signaling the remote computer that an error occurred, and 
requesting that the block of data be sent again.  If errors occur, your 
final Baud Rate may seem to be much lower than that set.

Transmission Bottlenecks

In any SLIP connection, several devices are transferring information 
in a "bucket brigade".  No matter the settings you use, the line can 
only go as fast as the slowest device.  For example, you might set 
your computer's baud rate to talk to its modem at 9600 baud.  
However, the modem itself might only be a 2400 baud modem.  
Therefore,  you'll only see 2400 baud transfers on your screen.

Data Compression

Finally, a factor which speeds things up instead of slowing them 
down.  Data compression is a means by which slow modems can send 
data faster than would normally be possible.  If your modem 
supports data compression (and this will be clearly indicated on the 
box at time of purchase, as it is a strong selling point), it will look at 
the data that it receives to see if there are any ways in which the 
data can be reduced in size.  For example, if it receives the letters 
"aaaaaaaaa", it might compress them into "9*a".  Of course, the 
modem on the other end of the telephone must know how to de-
compress this data correctly.

COM Ports

Most IBM-compatible computers come with four possible 
"Communications Ports".  Usually only one or two of these is built in 
and others must be added separately.  These built in ports are COM1 
and COM2.  If you are not sure which port your modem is connected 
to, start with COM1, then try COM2.  If nothing works, you may have 
to seek assistance in determining your setup.

COM 1

The most commonly-used Communications port is COM1.  Click on the 
COM1 button if your modem is plugged into the COM1 port.  You'll 
have to figure out what plug-in on your computer is the COM1 port 
as they are rarely labeled.

If your computer has COM1 and COM2 already occupied, or you have 
some special cards that use the COM interrupts, you may have your 
COM ports at a non-standard address (see below).

COM 2

COM2 is also frequently used for communications.  If you have a 
mouse connected to COM1, you will want to use COM2 for 
communications.

COM 3 and COM 4

COM3 and COM 4 are not as commonly used as COM1 or COM2.  Part 
of the reason for this is that these ports use the same Interrupt 
signals as COM1 and COM 2 (Interrupts 4 and 3, respectively).   For 
example, if you have a device on COM1, you cannot put a device on 
COM3, because whenever the computer sends a signal to COM1 both 
devices will try to answer at once.

Nonstandard Ports

For individuals who have filled their standard (COM1 through COM 4) 
ports, several nonstandard ports are available, but not 
recommended:

COM5 is actually COM3, but using interrupt level 2.

COM6 is actually COM4, but using interrupt level 2.

COM7 is actually COM3, but using interrupt level 5.

COM8 is actually COM4, but using interrupt level 5.

Real techweenie stuff

Below is a chart of I/O addresses and Interrupt levels.  Most users
won't have to worry about this.  If you have your COM  port at a 
non-standard I/O address or interrupt level, then you'll have to 
consult this chart to figure out what COM port your serial port uses.

Unfortunately there are two sets of these numbers, one for non-
MicroChannel PC's and one for MicroChannel PC's.  MicroChannel PC's 
are mainly IBM PS/2 models 50 and above.

MicroChannel				ISA/EISA
PORT	IRQ	I/O Address	PORT 	IRQ	I/O Address
com1	4 	03f8 		com1	4	03f8
com2 	3	02f8 		com2	3	02f8
com3	3	3220		com3	4	03e8
com4	3	3228		com4	3	02e8
com5 	3	4220		com5 	2	03e8
com6 	3 	4228		com6	2	02e8
com7 	3 	5220		com7	5	03e8
com8	3 	5228		com8	5	02e8

Modems

It's important to know what kind of modem you are using when 
establishing a SLIP connection.  The Modem List displays built-in 
scripts for operating Hayes, ADI-100, and other kinds of modems.  It 
is possible to build customized scripts if your modem is not listed 
(see SCRIPTS below).

HAYES

As the standard by which other modem command sets are measured, 
the Hayes script ought  to be compatible with any modem.  Of course 
it isn't, which is why customized scripts are needed (see SCRIPTS 
below).

ADI

The University of Minnesota's internal telephone system operates 
over a digital network, allowing both voice and computer data to be 
transmitted over the same phone line, and allowing for the routing of 
computer data into the SLIP server without using a standard modem.  
Instead, offices at the University which do not yet have a standard 
network connection can order an ADI-100 transceiver with MKO 
(Machine Keyboard Originate) enabled.  For information about this 
procedure, U of M staff can contact the Telecommunications 
Department at 6-7800.

The ADI script is to be used with these ADI-100 connections.

Other

We will add other modem scripts to this list as time for testing 
allows.  If you create a customized script which you think would be 
useful to others, please feel free to send it to us at

	slip@boombox.micro.umn.edu

Advanced Configuration

Parity

Parity Checking is the means by which your computer can make sure 
that transmitted data is getting through correctly.  Different hosts 
need different parity settings.

Odd Parity means that the parity of all data words received should 
be set odd.

Even Parity means that the parity of all data words received should 
be set even.

Mark Parity means that no error checking is conducted, but the 
parity bit is always set to one.  Nobody uses it.  There is no truth to 
the rumor that Mark Parity invented the first modem.

Even fewer people use Space Parity than Mark parity.  Space parity 
means no error checking is conducted, but the parity bit is always
set to zero.

Stop Bits

Stop Bits are used to separate words of data.  The more stop bits  
employed, the longer the pause between data words.  This used to be 
an issue when data transmission technologies were new, but 
nowadays stop bits are not quite as important.  One is usually 
sufficient.

Two stop bits are usually more than are necessary.

Handshaking

Handshaking is the means by which two computers tell each other 
when they are able and unable to accept further data.  There are two 
ways to do this: Software and Hardware.

Software Handshaking

Software handshaking controls data flow by sending a signal called 
"XON" for "Transmit On" (usually a control-Q), or "XOFF" for "Transmit 
Off" (control-S).

The problem with this method is that if you send an XON or XOFF  
signal inadvertently (for instance, by sending a binary file which 
happens to contain a control-S character), your computer will 
interpret this as an XOFF and stop sending.

So for SLIP transmissions, it usually best to use either NO 
handshaking, or to use the other method of handshaking, Hardware 
Handshaking.

Hardware Handshaking

Hardware handshaking depends on the actual pins connecting your 
computer  to your modem to control data flow.  If you are using a 
cable which does not have wires connecting pins number 4 and 5 (on 
a 25-pin cable or 7 and 8 on a 9-pin cable) , hardware handshaking 
will not function.  The two signals carried on these pins are Clear-To-
Send CTS and Request-To-Send RTS.

CTS, or Clear-To-Send Handshaking, sets pin 5 of your serial port 
either ON or OFF depending on whether or not your computer is 
ready to receive more data from your modem.

RTS, or Request-To-Send Handshaking, sets pin 4 of your serial port 
either ON or OFF depending on whether or not your computer is 
ready to send more data to your modem.

If you are using a modem with data compression, set CTS and RTS 
handshaking ON, otherwise leave it OFF.

Signals and Cables

There are nine signals which comprise the serial communication 
signals from your computer to its modem (see table below).  These 
signals are carried between your computer and modem by a modem 
cable.  While nine signals are available, it is possible to skimp and get 
by on only four of the nine signals:  SD, RD, DSR and DTR.  Sometimes 
cable manufacturers will produce inexpensive cables by only running 
four wires carrying these signals between the ends of the cable.   
SLIP communications are much more demanding, and require all 
nine signals to be present.  Be sure to use serial cables with all signal 
lines in place.  One way to be sure is to purchase "flat" or "ribbon" 
cable, which carries all 25 lines in a flexible plastic ribbon.

Table.  Serial communication signals and pins.
	Signal Description	Code		25 Pin #		9 Pin #
	Transmitted Data	SD		2			3
	Received Data		RD		3			2
	Request to Send		RTS		4			7
	Clear to Send		CTS		5			8
	Data Set Ready		DSR		6			6
	Signal Ground		SG		7			5
	Carrirer Detect		CD		8			1
	Data Terminal Ready	DTR		20			4
	Ring Indicator		RI		22			9


Plugs

There are two kinds of plug to be found on modem cables.  The first 
kind, 25-pin, is a wide, flat plug with two rows of pins.  Only nine of 
these signals are used for serial communications, even if all 25 pins 
are present (sometimes the unused pins are left out of the plug 
itself).

The second kind of plug is a 9-pin connector.  It has one pin for 
every signal necessary for serial communications.  The table below 
indicates which pins carry which signal on each kind of plug.

Note that hardware handshaking will only work if the cable between 
your modem and PC has the proper wires carrying Request to Send 
and Clear toSend (pins 4 and 5 on a 25-pin connector, 7 and 8 on a 9-
pin connector) running from end to end.  If your modem cable does 
not carry all nine signals, you will need to purchase a cable with all 
lines in place.	

Dialing

Touch tone dialing is present when you can place a call by dialing 
with musical tones.  Sometimes you might think you have touch tone 
because you have a fancy telephone which has buttons; but if it 
doesn't actually complete your call until doing a lot of clicking, it's 
likely converting your button-pushes into pulse signals.

Determine which type of telephone service you have, and select 
either Tone or Pulse .  When in doubt, use Pulse.

Initialization String

You may wish to send some command to the modem to meet some 
special need. The string you type in this box gets sent to the modem 
just before dialing is done.  It is sent after the modem script has sent 
its options.

SLIP (F5)

Configuration Window

A SLIP server is usually implemented with some form of security.  
PHONE can be configured to respond correctly to your SLIP server's 
security system by entering the proper values in the fields in this 
window.

User Name

Enter your username as 

	username@computer.full.tcp.name

for example:

	joe0024@student.tc.umn.edu

Password

Enter the password that goes with your username here. 
It will not be displayed on the screen, so be sure to get it right.

Phone Number

Enter the phone number in this box.

As of Feb, 1993 some commonly used phone numbers (in Minnesota) 
are:

	¥ The Univ of Minn SLIP server for most modems is 626-1920.
	¥ The Univ of Minn SLIP server when on-campus is 6-1920.
	¥ The Univ of Minn SLIP server for ADI modems is 3-0291.
	¥ The MRNET SLIP server is 626-7638.

If you are in a different area code, you'll need to prepend the area 
code to these numbers.  In some area codes you also need to prepend 
a 1.

Special Dialing Considerations

If you need to dial out from a hotel phone, or an office telephone 
system, you may have to prepend a 8 or 9 to dial out of that local 
phone system.  You may also have to add a comma to add a bit of 
delay after the 8 or 9.  For example, to call the the U of M from a 
hotel in California, you may have to specify:

     8,1,612,626-1920

If you have call-waiting, your SLIP connection may occassionally be 
interrupted by incoming telephone calls.  Depending on the service 
available in your area, you may be able to suspend call-waiting for 
the duration of one call.  This is accomplished with a special dialing 
sequence which precedes the actual phone number

	Tone		Pulse
	*70		1170

To suspend call waiting from an off-campus telephone calling the 
University of Minnesota, you would enter the phone number as

	*70,6261920

or if using pulse dialing

	1170,6261920

You may wish to test for this feature by hand before incorporating it 
into your dialing sequence.

Server Window

A SLIP server is the remote computer which will be your gateway to 
the TCP/IP network.  If more than one gateway exists, this window 
will holds the list of gateways to choose from.  If only one gateway 
exists, this window will not appear.  This list will vary from one local 
network to another.

University of Minnesota students & staff should pick the UofM 
server.

Time Display

For your convenience, the current time is displayed in the upper 
right-hand corner of the screen.  This can be a useful device for 
determining the timing of events if you happen to be writing a 
custom script (see SCRIPTS below).

The Lower Status Bar

The lowest line on the screen is a status bar which will change to 
offer you assistance with whatever portion of the program you 
currently have active.  This bar has two parts:

Active Keys display

The left-hand portion shows active help keys highlighted in red, with 
their names beside them in black.  For instance, at any time you can 
press the F1 key to get Help with the current active item, so the 
Active Keys display will usually show at least "F1 Help".

Context-Sensitive display

The right-hand portion of the Lower Status Bar indiciates the 
purpose of the currently active item.  For instance, if the cursor is in 
the Transaction Log window, the right-hand portion of the Lower 
Status Bar reads "This window displays what is happening during a 
login.", which is the function of the Transaction Log window.

Transaction Log Window

This window is where you can watch the interaction between your 
computer and the remote computer which will provide SLIP service.

Labelled horizontal status bars indicate when important steps in the 
login sequence are completed or fail to complete correctly.

Command-line operations

From the DOS command line, you can type

PHONE DIAL

to connect to the SLIP server, or

PHONE HANGUP

to disconnect from the SLIP server.  In some cases

PHONE FORCE <command>

where <command> is either DIAL or HANGUP may be necessary.  Try 
these if PHONE is complaining that the modem is misbehaving.

PHONE WRITE

PHONE comes with several script files built in.  These include the 
individual modem dialing scripts such as HAYES and ADI (see The 
Primary Screen: Setup: MODEM above), plus the HANGUP command.
The PHONE WRITE command will extract these scripts into a file 
called PHONE.CMD.  For more information, see the SCRIPTS section 
below.

PHONE ?

Prints a brief description of the PHONE command-line options.

Scripts

Until now, using SLIP was difficult.  First you had to call a SLIP 
modem pool, using a modem and a communications program such as 
PROCOMM. Then you would tell the modem pool that you wanted to 
use SLIP, and receive an IP address for the session.  Then you would 
exit the communications program, being careful not to disconnect 
your modem (by leaving DTR on for you experts), and edit a 
configuration file, adding your IP address to the configuration.  
Finally, you would load your packet driver and you could use Telnet 
or FTP.

This was very cumbersome.

The PHONE program is designed to automatically connect to a local 
SLIP server, configuring your computer and loading the UMSLIP 
packet driver.  Ideally you can establish a SLIP connection simply by 
using the command:

	PHONE DIAL

from the DOS command line, or a batch file, and be connected 
"automagically" .

Built-in scripts

To accomplish this task, PHONE understands a built-in scripting 
language.  This lets you custom design a script to work at your 
particular site.  You have to customize the script for each site for two 
main reasons: (1) Each model of modem is slightly different and 
needs different commands.  (2)  Each SLIPserver will have its own 
custom prompt lines and will require different information for 
logging on and entering SLIP mode.

We supply some generic scripts that work with Hayes-like modems 
to dial our local U of MN SLIP server.  You can probably customize 
this script for your particular site.  See the scripting language guide 
which follows.

How to make custom scripts

PHONE comes with several built-in scripts.  However, these scripts 
are not likely to work for anyone who is not at the University of 
Minnesota.  Therefore, it will be necessary for many people to create 
customized scripts.

PHONE WRITE

The first step in the process of creating customized scripts is to write 
the built-in scripts out to a file.  It is often easiest to customize an 
existing script rather than to start from scratch.  The PHONE WRITE 
command writes the scripts out to the PHONE.CMD file.

PHONE.CMD

If the PHONE.CMD file is present in the directory with PHONE.EXE, 
PHONE will read in PHONE.CMD rather than its built-in scripts.  
With the SLIPScript language (see below), it's easy to create and use 
customized SLIP scripts.

The SLIPScript Language

SLIPScript is a simple language for setting up the serial line, sending 
characters, waiting for a character string.

Each SLIPScript script must contain at least two procedures, named 
"Dial" and "Hangup".  The "Dial" script should contain commands to 
open the SLIP connection.  The "Hangup" script should contain 
commands to close the serial connection. 

SLIPScript Elements

# comment

You can enter any text after a # character.  This text will be ignored 
by the command processor.

The # comment can be on a line by itself, or appended to the end of 
another command line.

command param1 param2 param3

SLIPScript commands consist of a keyword.  Valid command 
keywords are:  Proc, EndProc, Send, Serial, Expect, DTR, Repeat, Flush, 
TimeOut, Wait, and Set.

Some commands take parameters.  Parameters are separated by 
spaces. If you need a space inside a parameter, enclose the whole 
thing in quotes ("").

The TimeOut, Wait and Repeat commands take a time in seconds.  
You can specify fractions of a second, i.e. 0.5 or 2.5 seconds. 

SLIPScript commands

Procedure and EndProcedure

The "Proc" statement  identifies the beginning of a procedure.  
Procedures continue until the next "EndProc" statement.
Example:
#
#     This is the shortest possible script
#
Procedure Modem.Hayes.Dial
EndProc   Modem.Hayes.Dial

The proc name has three parts, separated by dots.  The first part is 
either "Modem" or "Host".  The second part is the name of the modem 
or host.  The third part is either "Dial" or "Hangup" for a modem 
script, or "Login" and "Logout" for a Host Script.

Join

The join command lets you continue execution in another script.  For 
instance, many modems need some initial setup commands, then 
they can join the standard Hayes modem script.  The join command 
eliminates much duplicate scripting.

Serial

The "Serial" command lets you set up the serial port.  You can choose 
which serial port to use, what baud rate to use, and choose even, odd, 
or no parity.  You can also choose whether to use hardware 
handshaking.  The parameters are:

COM port
Selects the COM port to use.

7 or 8
Selects 7 or 8 data bits.

9999
Any string of 3 or more digits means a baud rate.  Valid values are 
300,1200, 2400, 4800, 9600, 19200, 38400, 57600.

E, O, N
Selects Even, Odd, or None parity.

hi+ or hi-
Sets input hardware handshaking on (+) or off (-).

ho+ or ho-
Sets output hardware handshaking on (+) or off (-).

Examples:

Serial Modem 1200		# simple 1200 baud modem
Serial Modem 38400 hi+ ho+	# fancy v32 modem


Notes:

Once established in SLIP mode, SLIP connections must be 8 data bits.  
You may have to choose 7 data bits first to talk to the modem, PBX, 
or the terminal server. 

YouÕll need hardware handshaking if you are using a modem with 
data compression.

YouÕll also need hardware handshaking if your modem auto-connects 
at a different baud rate than the one it is talking to.  Otherwise it is 
safer to use the default ( hi- and ho-).  See the section on Hardware 
Handshaking for a discussion of hardware handshaking.

You may lose some incoming characters if they arrive just as the 
Serial command is being executed.  It is best to place the serial 
command at spots where you know is quiet.

Send

You use the Send statement to send out a stream of characters.  
Anything you place on the same line after the "Send" keyword will 
go out the serial line.  It is best to put the string in quotes ("") to 
avoid ambiguity.

There are a few special characters that have special meaning:

< (less-than sign)

  The less-than sign means send an ASCII "Return", or end of line 
character.  For example, to get the attention of a Hayes-style modem: 

 		Send AT<

% 

The percent sign means to insert a variable in place of the % sign.  
The character following the %  is a letter from a-z identifying the 
variable.
 Predefined variables include:

 %n
for the phone number entered into the SLIP user dialog box.
 %u 
for the user name entered into the SLIP user dialog box.
%p
for the password entered into the SLIP user dialog box.
 %s
for the custom init string entered into the SLIP modem dialog box.

^ (caret sign)

The up-caret lets you send any control character.  For instance you 
can get the attention of a ADA 2020 modem by sending Control-Q:

		Send ^Q

To send the caret character itself, send two carets together (e.g. ^^).

# 

Remember that the # starts a comment.

You can define other variables with the"Set" command

There is a 1 second pause before each send command.  There is a 
1/10 second pause between sending out each character, in order to 
simulate typing speed.

SendDT

You use the SendDT statement to send the two forms of the dialing 
command.  The first parameter is the pulse dialing command, the 
second the tone dialing command.  For a Hayes modem, this is:

		SendDT 'AT DP %n' 'AT DT %n'


Expect

The Expect statement has two parameters.  The first is a string of 
characters to wait for.  The second is an error message to display if 
the string is not seen.  The strings are not case-sensitive.

It waits for the default time of 10 seconds.  If it doesnt get the 
specified string in that time, the script displays the error message, 
quits execution and SLIP signals connection failure to the application.

Example:  Getting the ModemÕs attention:

		Send 'AT<'
		Expect 'OK' 'Did not get OK'


Reject

The Reject statement detects error conditions. The Reject statement 
has two parameters.  The first is a string of characters to wait for.  
The second is an error message to display if the string is seen.  The 
strings are not case-sensitive.

You can have any number of reject statements.  It waits for the 
default time of 10 seconds.  If it does get the specified string in that 
time, the script displays the error message, quits execution and SLIP 
signals connection failure to the application.

If you dont specify an error message, the current "alert" string is 
used.
Example:  Getting the ModemÕs attention:

		Send 'AT DT6-1920<'
		Reject 'BUSY'          'Phone line is busy'
		Reject 'NO CARRIER'    'No modem answered'
		Expect 'OK'            'Did not get OK'

TimeOut

You can change the timeout interval for the next Expect statement 
with the TimeOut command.   The TimeOut command takes two 
parameters.  The first is the number of seconds to wait before timing 
out.  The second parameter is an error message to display upon 
timeout.

For example, if your phone system is slow to dial and connect, you 
may want to say:

		Send 'AT DT 636-1630<'
		TimeOut 45  'Did not get connect in 45 seconds'
		Expect 'CONNECT'

Repeat

The repeat command is useful when you have to retry sending a 
string of characters to get attention.  For instance, many systems 
require an indeterminate number of ASCII Return characters to 
detect your baud rate.  The repeat command makes this easy.  You 
can specify the number of repeats and the time interval between 
repeats:

Example: to get the attention of a certain terminal server:

		Repeat  '<'    'access:'  20 2.5

Will send "<"  which is the special character meaning ASCII Return, 
until it receives the string"access:".  It will try up to 20 times, with a 
2.5 second pause between attempts.


Or to get the attention of a certain modem that is slow to detect the 
baud rate:

		Repeat 'AT<' 'OK'  5 1.0


You need not specify the repeat count and pause time.  The default 
repeat is 10 and default pause is 1.0 seconds.

Since the repeat command takes several parameters, you should 
enclose strings in quotes to avoid any confusion as to which 
parameter is which.
Example:

		Repeat "<"  "Please log in now:"

Wait

The wait command pauses for the specified number of seconds.  This 
is usually the wrong way to control interactions.  It is better to use 
the "Expect" command to wait for a particular prompt.  But 
sometimes a pause is the only way to meet some login requirement.

  Example:  Calling out through a slow PBX

		Send "Dial 8<"    	# Get an outside line
		Wait 5.0			# Wait 5 sec for slow PBX
		Send 'Dial %n'		# send the phone number

DTR

Some modems or PBXÕs don't respond until the DTR line (RS-232 pin 
20) is asserted.  The DTR command lets you control the DTR line.  
Examples:

		DTR On          	Asserts DTR
		DTR Off		Drops DTR
		DTR			Drops DTR, waits 1 second, asserts DTR


Note that many serial cables send the DTR line out pin 8, requiring a 
special cable or adapter to move this to pin 20.  See Signals and 
Cables above.

Flush

Sometimes you want to ignore any pending input characters as they 
may be misleading.  The Flush command throws away any pending 
input characters.  You often want to do this when you expect some 
"logon banner" that might have some unpredictable text.  Flush that 
stuff before you try to do an "Expect".

Example:

		Send 'AT DT 636-1630<'
		TimeOut 45
		Expect 'CONNECT'	# wait for modems to connect
		Flush
		Repeat "<" "login:" 20 1.0   # hit return til login

Set

The set command lets you set up variables that you use again and 
again.  You can set them up in one place instead of repeating them 
over and over.   The syntax is:
Set x something

Sets the variable x to the value "something".  x can be any letter from 
a to z.  Something can be anything including other % variable 
references.

Example:  Your terminal server prompts with "Server #0001 for the 
Main Campus:"

		Set %h "Server ##0001 for the Main Campus:"
		Send 'ATDT 636-1630'
		Expect 'CONNECT'
		Repeat '<' %h 20 2.0
		Send 'terminal NoEdit<
		Expect %h
		Send 'terminal FlowControl None<'
		Expect %h
		Send 'terminal baudrate 9600<'
		Expect %h
		Send 'terminal databits 8<'
		Expect %h

Writing a script

If possible, modify an existing script instead of writing a new one 
from scratch.  The best way is to try connecting with a terminal 
emulator, saving the output to a file.  This log file will guide you in 
writing the script.

You'll have to note places where you had to pause for something to 
respond.  Writing a script can be easy or difficult.  Many dial-up 
ports a bit non-deterministic and you'll have to play with the Repeat 
command until things work right.

When you write your script, make use of the variables the user has 
set up in the PHONE menu, i.e. don't hard code "636-1630" as the 
phone number, use the %p phone number variable.

Debugging a script

Try out scripts by choosing them in the Modem settings dialog box. 
PHONE will run your Dial script.  It may fail  at first.  The most likely 
failure is an Expect command failing.  If an "Expect" command fails, it 
will show you what it expected and what it actually received.  Edit 
the script and try again.

Remember to send a Return at the end of lines that expect a Return.  
The Send command never sends a Return for automatically.

Alert

You can put up custom messages in case of error conditions.  With 
the "Alert" command you can specify a message that will be put up if 
an Expect command fails. e.g.:

		Alert "Your modem may not be on?"
		Send 'AT<'
		Expect 'OK'


If PHONE doesnt get an "OK" in the specified time,  the user will see a 
dialog box with "Your modem may not be on?".

Message

You can also put up an informative message to the user to keep them 
appraised of how the dialing procedure is going.  Normally PHONE 
displays each command as it is executed.  If you use the Message 
command, that string will be displayed instead of the commands.  
Your message will remain displayed until you change it with another 
Message commmand, or until the script ends. e.g.:

		Message "Getting the modem's attention"
		Send 'AT<'
		Expect 'OK'
		Message "The modem is responding!"

Let us know about your scripts.

We will add other modem scripts to our list as time for testing 
allows.  If you create a customized script which you think would be 
useful to others, please feel free to send it to us at

	slip@boombox.micro.umn.edu