File  RMKIFACE.DOC
------------------		Chris Kennington	8th July 1985.



		Research Machines Kermit Software Interfaces
		--------------------------------------------


0.  Structure of RM Kermit.
    -----------------------

     The bulk of RM Kermit is written in standard C, designed to be
portable between micros and micro operating systems.  The actual
implementations carried out at RML are for the RML 480Z, a Z80-based
micro running under CP/M, and for the RM Nimbus, a 80186-based micro
running (in this instance) under MSDOS.  Since the performace and
acceptability of Kermit depends heavily on its handling of keyboard,
screen and communications line, no attempt was made to use standard
CP/M or MSDOS functions for these purposes.  Instead, a software
interface to these routines was specified and hardware-dependent
low-level routines coded to connect this interface to the necessary
functions.  (Due to the various possible hardware configurations,
there are in fact several different sets of such routines.)

     There are also a small number of organizational procedures
which may differ according to the micro OS used and other 
characteristics of the environment.

     Since a set of routines specific to the implementation have
to be created and included, opportunity was taken to make some of
the texts displayed also variable, so that help and other information
is more closely appropriate to the version being run.

     This document describes these interfaces and lists the texts.
For further information about specific cases, see file RMKGEN.DOC.



1.  Keyboard/Screen Interface.
    --------------------------


1.1  Screen-Handling.

     Kermit mostly divides the screen into a 4-line parameter area
at the top, a fixed divider line, and a 19/20-line scrolling area
occupying the rest of the screen.  When in one of the menu modes,
a further 5-line section plus divider is fixed at the bottom, leaving
14 or 15 lines for the menu.

     Some optimisation of output has been done, to provide the fastest
display of information compatible with reasonable flexibility.  Calls to
printf() are used where it is necessary to format binary numbers
and variable strings into other text, but other procedures are used to display
fixed strings and individual characters at the current cursor position.
All map into calls to the special screen-output procedure outc(), via a
formatting routine outfc() which expands tabs etc. and deals with paging.
Output of individual characters and strings to fixed screen-locations
is handled by other procedures.

     All this logic deals with output destined for the physical screen.
The built-in C-function putchar() remains the correct procedure for
output of escape-sequences etc. which are in fact intercepted by the
OS or the micro-firmware and interpreted by it rather than being passed
for display.


1.2  Keyboard-Handling
  
     There is only one procedure required for reading the keyboard, kbdin();
it is of type char, and returns immediately with or without a character.
It is assumed that the keyboard is buffering any characters which are input
more rapidly than they are read out (though there is no expectation of readout
falling seriously behind input).  Kbdin() does not deal with null characters
(ctl-@), since the return with this is indestinguishable from the return
without a character.  See below for the data which it is expected that
the arrow and F keys will return.


1.3  Procedures.

     The keyboard/screen procedures which are used by Kermit are as follows
(in all cases, the range of values taken by char variables is assumed to be
from 0 to 255):-

  curset(line,col)	position cursor
	char	line, col;
    No return-code.

  cursor(sw)		remove/replace cursor
	char	sw;
    If sw = 0, the cursor is removed from the screen; the coordinates
      of the current position continue to be manipulated (by data-output
      or otherwise), even though the cursor is not on display.
    If sw != 0, it is taken as representing a cursor-character to be
      displayed @ the current position. 
    No return-code.

  char kbdin()		read char from keyboard
    Returns char in range 1-255, or 0 if no character available.

  keyconn()		set keyboard for connect-mode
    Performs any reinitializations needed for connect-mode
      (when the characters to be sent from certain keys may
      differ from those defined below).
    No return-code.

  keyinit()		initialize
    Sets up both keyboard and screen (see below).
    No return-code.

  keyrest()		restore
    Restores keyboard and screen to their normal state.
    No return-code

  outc(ch)		character to screen @ cursor-position
	char	ch;	character
    No return-code.
    A very limited set of control characters are honoured,
	see below for details; others are ignored.
    Characters with the top bit set are displayed as inverse
      video equivalents of those without.

  screen(top,bottom)	define scrolling-area
	char	top, bottom;
    No return-code.
    This defines the scrolling area of the screen to be from "top"
      to "bottom" inclusive.  The parameters may be assumed correct,
      except that bottom > 23/24 implies the lowest possible line.
      (Line-numbering 0 - 23/24.)
    The scrolling area is full screen-width.

  scroll(n)		scroll screen up/down
	int	n;
    No return-code.
    The scrolling area of the screen is scrolled up or down by the
      number of lines defined by n.  n > 0 implies normal scrolling
      (data moves up); n < 0 is the opposite (data moves down);
      n = 0 is a no-op.  Blank lines are scrolled in at top or bottom,
      so a scroll of more than the size of the scrolling area is 
      a clear-screen.

  vtout(loc,ch)		character to screen @ specified position
	int	loc;	screen-position (in HL format as defined below)
	char	ch;	character
    No return-code.
    All characters are treated as printable.  For characters in the
	range 0-31 those defined for the RML 480Z are assumed, but
	any similar set should be acceptable.

  vtline(loc,str)	string to screen @ specified position
	int	loc;	screen-postion, as above
	char   *str;	pointer to string
    No return-code.
    All characters treated as printable, as above.  If the string runs
      off the edge, the end is lost.


1.4  Cursor Definition.

     In defining cursor positions, "HL format" means line*256 + col.
In either HL format or when specified as 2 parameters,
line and column are in range 0-23 (or 0-24) & 0-79 respectively, and refer
to the whole screen, i.e. (0,0) is the top left-hand corner, irrespective
of scrolling-area arrangements.  Validity checks are reduced to a minimum
(taking values > max to be = max and < 0 to be = 0), since Kermit is a
(presumably) developed program.


1.5  Control Characters.

     CR (0x0d) is defined to move the cursor to the left margin, then move
it DOWN.  LF (0x0a) is defined to move the cursor straight down.  
The UP (0x0b) & DOWN (0x0a) cursor movements cause screen scrolling if they
attempt to go off the scrolling area.  The RIGHT (0x18) & LEFT (0x08) cursor
movements are no-ops if the cursor is already on the margin.  Attempting to
store a character (by outc(ch)) when the cursor is at the right margin
causes a "CR" to the beginning of the next line (with scrolling
if on the bottom line).  DEL (7fH) is defined as a destructive
backspace, i.e. it deletes the character (if any) to the left of the
cursor, then moves the cursor LEFT.  Overtyping an existing character
has no side-effects (i.e. there is no "insert" mode).


1.6  Initialization.

     Screen initialization implies clearing, homing the cursor to top
left, and setting full-screen scroll.

     Keyboard initialization includes switching off any specially-treated
characters such as ctrl-A & ctrl-F.   Kermit uses the arrow-pad and F-keys;
the characters to be returned (other than in connect-mode), with and
without SHIFT, are:-

				      unshifted	       shifted
				      ---------	       -------
		arrow right		0f2H		0d2H
		arrow left		0ecH		0ccH
		arrow up		0f5H		0d5H
		arrow down		0e4H		0c4H

		F1			0e2H		0c2H
		F2 (TAB)		 88H		 88H
		F3			0eeH		0ceH
		F4			 9bH		0bbH

		DEL/DELT		0x7f		0xff




2.  Communications Interface.
    -------------------------


2.1  Manner of Working.

     RM Kermit makes no assumptions about whether polled or interrupt-driven
communications are in use.  Procedures return immediately (i.e. they do
not wait for data to be received or transmitted) with a flag indicating
success or error.

     In one of the implementations there was a hardware requirement
to quiesce the communications before issuing any commands to the
disk-handling parts of CP/M.  A call s4sleep() was therefore provided,
and is called before all disk operations.  It is a side-effect of any
call to the active procedures s4get(), s4put() or s4reset() to wake up
(un-sleep) the communications.

     The interface was designed to be used by other programs as well as
Kermit.  This has resulted in the existence of parameters which are
superfluous, but must be set as shown.  All procedures are type integer,
and return < 1 for an error; success is indicated by 0 or 1.  A call to
any routine when comms are not initialized is an error (-1); in most other
cases the value returned is that of a status-word (see below) which
always has the top bit set.


2.2  Procedures.

    s4break(len)	/* send "break" to comms line		*/
	char	len;		/* duration in sec/8		*/
      (this procedure is not expected to return until the break
	has been completely sent.)

    s4get(n,buff)	/* read character from comms line	*/
	int	n;		/* number of chars available	*/
	char	*buff;		/* buffer to receive chars	*/
      (in Kermit the value of n is always 1)
      returns 0 if no character available, else # of chars actually
	read (<= n), else error-status.

    s4get7(n,buff)  /* read stripped characters from comms line	*/
	int	n;		/* number of chars available	*/
	char	*buff;		/* buffer to receive chars	*/
      as s4get(n,buff) except that it strips the top bit;
	calls to the two may be intermixed.

    s4go();		/* open/initialize comms routines	*/
      may be called again after s4stop() to reopen comms;
	is a no-op if already open.

    s4put(n,buff)	/* write characters to comms line	*/
	int	n;		/* number of chars available	*/
	char	*buff;		/* buffer containing chars	*/
      (in Kermit the value of n is always 1)
      returns 0 if unable to write because line is busy,
	else # of chars actually written (<= n), else error-status.

    s4set(options,control); /* set facilities			*/
	int	options;	/* facilities-word as defined	*/
	char	control;	/* DTR & CTS bits of Z80sio WR5	*/

    s4sleep();		/* deactivate comms routines		*/
      provided for cases where use of disks and communications are
	mutually exclusive, otherwise may be a no-op.

    s4speed(code)	/* set speed of comms line		*/
	char	code;		/* RML speed-code, 0-9		*/
      this routine may be called before s4init().

    s4stop();		/* close down comms routines		*/
      this routine is a no-op if comms are already stopped

    s4test();		/* test status of communications	*/
      returns status-word as defined but with top bit set,
	hence always <0.


2.3  Returned Status-Word.

     This integer was originally a bit-pattern with meanings assigned
to permit careful control of communications.  Kermit only requires that
a negative value (top bit set) should be returned if there is an error. 


2.4  Option-Word and Control-Byte.

     These were also originally designed with a wide range of possibilities.
The only bits of significance to Kermit are as shown below; all other
bits may be ignored.

     Option-word:
		 0  -  RTS/CTS flow-control to be used
		 1  -  XON/XOFF flow-control to be used
		8/9 -  Parity-Generation on/off

     The 2-bit code for parity is:
		0  -  Generation not required
		1  -  Enforce odd parity
		2  -  Enforce even parity
		3  -  Enforce mark parity

     The only bit of the control-byte which is significant is bit7;
this is set to 1 to raise DTR or an equivalent signal, 0 to drop it.


2.5  Speed-Codes.

     The following speed-codes are defined (though not necessarily
all implemented in any given version):-
			
		0  -	110baud (2 stop-bits)
		1  -	300baud
		2  -	600baud
		3  -   1200baud
		4  -   2400baud
		5  -   4800baud
		6  -   9600baud
		7  -  19.2Kbaud
		8  -  40.8Kbaud
		9  -	 75baud

     There is no provision for split-speed working, nor for
half-duplex line turnaround.  8-bit data is always set, and
1 stop-bit except at 110baud.




3.  Miscellaneous Interface.
    ------------------------

     The following miscellaneous procedures are called by Kermit to
perform system-oriented functions:-


  cpmgo()		/* return to micro OS		*/
    this call is used instead of "exit()" to permit a clean return
	to the micro's operating system after carrying out any
	required housekeeping.

  fpanel()		/* debug display		*/
    this call is executed after an "ESC-F" break-in to access
	the micros's built-in lowest-level debugging display.
	It may be a no-op if no such facility is available
	or required.

  unsigned getram(n)	/* get storage			*/
      int  n;			/* # of bytes required	*/
    this call is used instead of "malloc()" to obtain dynamic
	storage so that the space occupied by initialization-code
	may be reused; it returns the start-address of the
	block of storage.  If unable to allocate it should
	printf() a failure-message and call cpmgo().  Storage
	once allocated is never released.

  netcool()		/* deactivate disk system	*/
    this call is made before reading or writing the communications
	line; it would normally be a no-op.

  s4env()		/* return environment		*/
    this call returns a small integer value to indicate the communications
	environment in which it is running.  The following values
	have been defined:-
		0  -  480Z via SIO4
		1  -  480Z via IDC
		2  -  Nimbus via Data Comms Controller (n.y.i.)
		3  -  Nimbus via Aux port
		4  -  Nimbus via Piconet
		5  -  480Z or Nimbus via RML Network (n.y.i.)
		6  -  non-standard
     (Any user extending this table will have to amend the entries
	in arrays locations[] and fuzz[] in RMKDATA.C)

     The versions of these routines in file RMKNIMB.C should be suitable
for most straightforward micros.



4.  Data Items.
    -----------

     There is no absolute need to change any of the texts displayed.
The versions found in files RMK480Z.C and RMKNIMB.C (for CP/M and
MSDOS systems respectively) may well be acceptable; the examples
below are those from the Nimbus version.

     Data items which should be supplied for display are as follows:-

char head1[]		text-string to identify program, e.g.
	    "  RM  NIMBUS  Kermit  File  Transfer  Program,";

char prompt[]		normal prompt to be displayed by RM Kermit (there is
	no ability to change this dynamically), preceded by CR, e.g.
	    "\rKmNimbus";

char eprompt[]		special prompt to be displayed after ESC break-in, e.g.
	    "\rKmF4> ";

char backto[]		final message to be displayed when Kermit terminates, e.g.
	    " OK - back to MSDOS; ";

     If these texts are altered, it is recommended that their lengths should
not be extended.


	*******************************************************