KERMIT for UNISYS A-Series Systems
October 1989

Authors:  Larry Johnson, Katie Stevens, Dave Squire
          University of California, Davis

Language: Algol
Version:  1.041
Date:     September 28, 1989

A-Series KERMIT Capabilities At a Glance:

     Local operation:                       No
     Remote operation:                      Yes
     Transfers text files:                  Yes
     Transfers binary files:                Yes
     Wildcard send:                         No
     Filename collision avoidance:          No
     Timeouts:                              Yes
     8-th bit prefixing:                    Yes
     Repeat count prefixing:                Yes
     Alternate block check types:           Yes
     Transaction logging:                   No
     Session logging:                       No
     Debug logging:                         Yes
     Act as server:                         Yes
     Advanced server functions:             No
     Command/init files:                    Yes
     Attribute packets:                     No
     Long Packets:                          Yes
     Windowing:                             No

Kermit is a program that does reliable file transfer between
computers over data communication lines and has been implemented on
many different machines, including microprocessors.  AS-Kermit,
written in Algol for Unisys A-series systems, communicates with
even the most minimal Kermit implementations.  The program source
is contained in one symbol file and does not require a separate
help file.  The program does not require any special datacom
support.

The file transfer protocol uses packets that are checksummed and
acknowledged, and are resent if errors are detected.  Packet
lengths are typically limited to 88 characters of data although
this version allows longer packet sizes to be specified.

In the narrative description that follows, there are several
references to AS-Kermit commands.  These commands are all described
in detail in the final section of this document.  Since one Kermit
does not a file transfer make, it is assumed that the reader is
familiar with at least one other implementation of Kermit, namely
the version that runs on the system communicating with AS-Kermit on
the A-series machine.


UNISYS File System

For Kermit users, the most important features of the Unisys A-
Series file system are character set, file title and file
structure.  Since AS-Kermit must be able to transfer files to and
from a large variety of operating systems there are commands to
allow users to control these attributes.

Character Set Conversion

The default character set of an A-Series file is EBCDIC.  Since
most micros and many other systems use ASCII, it is necessary for
AS-Kermit to translate between these character sets.  When
receiving a file, characters are unconditionally translated from
ASCII to EBCDIC.  When sending a file, AS-Kermit uses the EXTMODE
of the file to control translation.  If the file is already ASCII
then translation does not occur, otherwise an EBCDIC file is
translated to ASCII.  This translation is not important if the file
being transferred is a text file, but since the conversion changes
the bit patterns of each byte, problems arise when the file
contains binary data.  The SET BINARY command is used to preserve a
full eight bit binary byte across the seven bit data path assumed
by AS-Kermit.

File Title Conversion

Since A-Series file titles are generally incompatible with other
computer system file naming conventions, there are provisions for
title conversion. When sending, AS-Kermit can change an A-Series
file title into one more compatible with other systems; for
receiving, almost any file name may be converted to a usable A-
Series file title.  The SET SEND ACTUAL-TITLE command may be used
to suppress the default conversion of file titles that normally
occurs when sending files.

A-Series file titles are of the form:

     (USERCODE)NAME1/NAME2/.../NAMEX  ON FAMILYNAME

     Up to 12 names, each containing up to 17 characters, may be
     specified.

Most micros have file names of the form:  namename.ext, where
namename may be up to 8 characters long, and .ext is an optional
name extension up to 3 characters long.

If the default conversion occurs when sending, the filename sent is
the name following the final slash in the A-series title (NAMEX in
the example above).  If the name following the slash is longer than
8 characters, a  period is inserted after the eighth character and
up to three more characters are used as the name extension.  If the
name is longer than 11 characters,  it is truncated.  The on-part
is not sent and the usercode is removed from the file title
regardless of the state of SEND ACTUAL-TITLE.

     A-Series file title:   (USERCODE)NAME1/.../LONGERTHAN11 ON MYFAM
     Sent as:               longerth.an1

Additionally, since AS-Kermit uses one or more blanks as a token
delimiter, files may not be sent that have blanks as part of a
quoted name, nor can an on-part be specified in a SEND command.  To
send a file from a named pack,  that pack must be part of a FAMILY
statement specified before running AS-Kermit.

When receiving files, file name conversion is controlled by RECEIVE
ACTUAL-TITLE.  If this attribute is set, the only modification AS-
Kermit makes is to translate all lowercase letters in the file
title to uppercase.  If the resulting name is not a valid A-Series
filename the receive will fail.  If this attribute is not set, AS-
Kermit converts the name supplied by the sender into a title with
the following rules:

     1)  Lower case is translated to upper case and extraneous
         slashes are deleted.

     2)  If a name is longer than 17 characters, it is broken up
         into multiple 17 (or fewer) character names separated by
         slashes.

     3)  Names that contain non-alphanumeric characters, including
         periods, are enclosed in quotes.

     4)     The new title can have no more than 12 names.

Since slash is used as a name separator, about the only string that
won't produce a valid A-Series title is one of all slashes.

     File sent as:     /justabitlongerthan17/"a/"//"zT"/abc.ext
     A-series title:    JUSTABITLONGERTHA/N17/"A/"/ZT/"ABC.EXT"

Unless the A-Series site runs AS-Kermit as a privileged program,
files can not be directed to another usercode.  To specify a
usercode and/or a named pack, RECEIVE ACTUAL-TITLE must be set and
a valid A-Series title specified with the usercode in parentheses
and/or the on-part following the name.

File Structure Conversion

The file system on an A-Series computer is based on fixed-length,
blocked records. Some other systems also use this method, but many
systems use variable-length records with a character such as a
linefeed for a record separator. The SET FILE commands control the
manner in which AS-Kermit converts between fixed and variable
length file formats.

For AS-Kermit to be able to open a disk file for sending, the file
must have FILEORGANIZATION of NOTRESTRICTED,  which is the default
for disk files on an A-Series system.

Sending Conversion

The default for AS-Kermit is to convert from fixed-length to
variable-length records and to insert the two character separator
consisting of <carriage return, linefeed> between records.  After
the possible translation to ASCII, variable-length records are made
by stripping trailing blanks and characters less than blank off the
end of the fixed-length record read from the disk file.  SET FILE
FIXED may be used to inhibit the stripping of these trailing
characters.

SET FILE RAW may be used to not only inhibit the stripping of
characters but to also inhibit the insertion of record separators.

Receiving Conversion

When receiving a file, AS-Kermit creates a diskfile with the
following defaults:  MAXRECSIZE = 15, BLOCKSIZE = 420, UNITS =
WORDS.  The SET FILE commands may be used to change these
attributes but they must remain compatible.  If a warning about
blocksize-recordsize incompatibility is given, the values must be
corrected before receiving a file.

AS-Kermit converts the received records to fixed length format disk
file using the following rules:

     1)  Any occurance of a linefeed is used to end a record. If
         the record received is shorter than a disk file record,
         it is padded with trailing blanks.  If the record
         received is longer than a disk record, it is split into
         two or more records, and the last one is padded with
         blanks if necessary. The linefeed is not included in the
         disk record.

     2)  Carriage returns are discarded. It is assumed that they
         are part of the record separator.

     3)  Tabs (HT) are converted to blanks. The tab positions are
         in 8-column fixed positions.  When a tab is encountered,
         blanks are inserted in the disk record to move to the
         next tab position.  The tab conversion can be disabled
         with SET FILE EXPAND-TABS OFF.  In this case, the tab
         characters are written into the disk file.

One other option exists for file reception.  SET FILE RAW ON may be
used to override the record and the character conversions mentioned
above. The disk file generated on the A-Series system is then a
byte-by-byte copy of the received file, translated to EBCDIC.
Setting  RAW ON  also sets EXPAND-TABS OFF.

Transfers fail if the sending Kermit tries to use the parity bit
for data.  The local Kermit should have its communication set up
for 7-bit if there are non-graphic characters in the file to be
transferred.  With some Kermits, this can only be done by setting
parity to "space".  Files containing EBCDIC characters that
translate into ASCII characters with a value greater than 127
cannot be sent by AS-Kermit unless BINARY is ON.

Running AS-Kermit

AS-Kermit must be run interactively, and only in remote mode.  This
means that AS-Kermit may not be used to call another computer.
Instead, the local system communicating with the A-series machine
must run its version of Kermit.  The local Kermit's terminal
emulator is then used to log-on to A-series Cande and to run AS-
Kermit.  Thus the user needs to be familiar with both AS-Kermit and
the Kermit version running on the local system.  The following
discussion, from the point of view of a user running a local Kermit
on a computer in communication with an A-series host, refers to the
user's system the local system.

The first step in any file transfer is to run Kermit on the local
system.  When beginning execution, most versions of Kermit load an
optional initialization file and then prompt for a command.  To
talk to the A-Series system, the CONNECT command is entered in
order to begin terminal emulation. The keyboard and screen of the
local system then act as a terminal and the user connects to the A-
series computer according to the method used at the particular
site.  This might consist of telling the local system modem to dial
out, or if the local system is directly connected to a network
switch, simply specifying the A-series host in response to a
"request" prompt.

Once connected, the user logs on to Cande and then runs AS-Kermit.
At UC Davis, typing "KERMIT" begins this execution, after which an
initialization file, if present, is read (see TAKE command).  A
prompt is then given to enter a command and file transfer may
begin.

To transfer from the A-Series, the command SEND followed by the
filename is entered.  The local Kermit  must then be put in receive
mode.  For most PC Kermits, "CONTROL-[ c", that is, CONTROL (CTRL)
and [ keys at the same time, then "c", escapes to command mode,
from which RECEIVE is entered in order to start receiving the file.
On a Macintosh, the FILE menu choice RECEIVE must be clicked. When
the transfer finishes, the Macintosh returns to terminal mode.
Other versons usually return to command mode from which a CONNECT
command is needed to restart terminal emulation in order to again
communicate with AS-Kermit and begin another transfer.

To transfer a file to the A-series machine, the RECEIVE command is
entered, then after returning to command mode on the local system a
SEND is entered.  If the files being sent to the A-Series system
need different record or block sizes, then the appropriate AS-
Kermit commands must be entered before receiving each file.

Server Mode

Server mode may be used to transfer several files in both
directions.  In this mode AS-Kermit takes commands from the other
Kermit instead of the keyboard. Instead of using SEND or RECEIVE
commands, the AS-Kermit SERVER command is used before going back to
command mode on the local Kermit.  The SEND command is used on the
local Kermit to transfer files to the A-Series system but the GET
command is used from the local Kermit to transfer files from the A-
Series system.  This method saves having to go back and forth
between the two Kermits to transfer files.

The FINISH command from the local Kermit terminates AS-Kermit, but
it is necessary to connect back in order to log off from the CANDE
session.  When exiting the local Kermit it may not disconnect from
the communication line so it is advisable to execute the HANGUP
command before the EXIT command.

AS-Kermit commands

Kermit commands can be abbreviated using the minimally
distinguishable string.  For example, as a command SE could be
either SET or SEND and produces an error;  R, however, suffices for
RECEIVE.

Abbreviations are context-sensitive.  As a command, SE is
ambiguous; however, as an argument to STATUS, SEND may be
abbreviated with S.  To check for ambiguous abbreviations, an
abbreviation followed by ? with no intervening space may be
entered.

EXIT    Exit from AS-Kermit, closing any open debugging log
        files.  AS-Kermit may be stopped in the midst of a
        transfer by typing ?DS or ?END.

HELP    Give a list of command verbs. Typing <command> ? gives
        the options available for that command.

QUIT    A synonym for EXIT.

RECEIVE Receive a file or group of files from the local Kermit.

SEND <filespec1> <filespec2> ... <filespecn>

        Send file(s) specified by <filespec1> <filespec2> ... to
        the local Kermit.  This command is used to send files to
        the local Kermit.  After entering the SEND command to AS-
        Kermit, the user returns to command mode on the local
        Kermit and gives the RECEIVE command.  If this is not
        done quickly enough, several "send-init" packets may
        arrive prematurely,  but AS-Kermit will continue sending
        them until it gets a response or until INITIAL-CONNECTION
        attempts have occured (see SET RETRY ).

SERVER  Act as a Kermit Server with default options, or with
        whatever options have been established by previous SET
        commands.  All options remain in effect as long as the
        server is running.  To change an option, the server must
        be shut down and restarted after changing the option.
        The AS-Kermit server may be shut down from the local
        Kermit with the FINISH command, or by connecting back to
        the A-Series system and typing ?DS.  In either case AS-
        Kermit terminates and must be run again to transfer more
        files.

SET <parameter>

        Set the specified parameter to the specified value.  Some
        parameters have their own parameters.


SET BINARY <value>

        On some systems, transmitting 8-bit data over a typical
        terminal line may result in corruption of the 8th bit.
        Kermit uses "binary quoting" to tell the receiver to
        store a byte with the high bit on.  This method involves
        extra overhead, and it should be used only when necessary
        to guarantee the integrity of the 8th bit of data.  A
        text file does not normally need the eighth bit
        preserved.

        <value> = ON:  Use "binary quoting" when transmitting
        bytes with the high bit on.

        <value> = OFF:  Do not send any "binary quotes" when
        transmitting.  The received value of the high bit is
        assumed to be arbitrary.  This is the default.

SET BLOCK-CHECK <d>

        AS-Kermit supports 3 different block-checks, called type
        1, 2 and 3.  Kermit uses block-checks to detect data
        corruption during transmission. The larger values of
        block-check type provide better protection against errors
        at the expense of more processor time used to calculate
        them.  For short packets of less than 100 bytes block-
        check type 1 is adequate.  For longer packets or noisy
        communication lines, larger block-checks may be used.
        The default block-check is 1.  Both Kermits must agree to
        use the same block-check if type 2 or 3 is to be used and
        not all Kermits support all types.

        <d> = 1, 2, or 3.

SET DEBUGGING <option>

        When KERMIT is not transferring files successfully, it
        may be useful to inspect the messages that are sent
        between the two Kermits, or the internal state
        transitions.  Debugging display cannot be done to the
        screen since AS-Kermit cannot run in local mode so debug
        information is written to a disk file.


        <option> = STATES:  Show the packet number and type or
        internal state for each packet.

             S     Send Initiate
             R     Receive Initiate
             F     File Header
             D     Data
             Z     End of File
             B     Break Transmission
             C     Transfer Complete
             E     Error
             A     Abort Transmission
             T     Timeout
             Q     Checksum Failure


        <option> = PACKETS:  Display the actual incoming and
        outgoing packets.  For a description of the packet
        format, see the Kermit Protocol Manual.

        <option> = LOG-FILE <filename>:   This option allows the
        name of the log file to be set, but the <filename>
        parameter can only be a single name.  The file has a
        default title of KERMIT/LOG or may be file-equated when
        running AS-Kermit (INTNAME = LOG).  If there has been no
        previous SET DEBUG command , this command also forces
        DEBUGGING <option> to STATES.  SET DEBUGGING OFF closes
        the log file, as does the EXIT, BYE, and FINISH commands.

        <option> = OFF:  No debugging information is displayed.
        If debugging was previously in effect, debugging is
        turned off and any debugging log file is closed.
        Debugging is OFF by default.

SET DELAY <d>

        Specify the delay, <d> seconds, before sending the first
        send-init packet.  This allows time to exit terminal
        emulation, put the local Kermit in command mode, and to
        enter the  RECEIVE command.  Normal delay is 5 seconds.

SET FILE <parameter>

        File parameters allow Kermit to control some attributes
        of the files being processed.  The FIXED parameter
        applies to files being read.  The rest of the parameters
        listed below apply to files being written.

        BLOCK-SIZE <d>:  Sets the number of UNITS per block for
        the receive file. to <d>.  Default is 420 UNITS/block.
        Also see RECORD-SIZE and UNITS.

        EXPAND-TABS <value>:  Since not all software and hardware
        on A-Series systems can deal with tabs, this option
        allows tabs to be expanded into blanks.  The tabs, fixed
        at 8 columns per tab, can not be changed.  Setting RAW
        turns this option OFF.

             <value> = ON:  Expand tabs into blanks.  This is the
             default.

             <value> = OFF:  Store the tab characters in the output
             file.

        FIXED <value>:  Most Kermits use variable-length records
        on their host machines. To be compatible with these
        systems, AS-Kermit converts fixed-length files on an A-
        series host to variable-length records by stripping
        trailing characters less than or equal to ASCII blank
        from each record before transmitting.  This  reduces the
        number of bytes transmitted.  FIXED only applies if RAW
        is OFF.

             <value> = ON:  Do not strip trailing characters.  Send
             all the data bytes.

             <value> = OFF:  Do not transmit trailing characters.
             This is the default.

        RAW <value>:  A-Series systems generally use fixed-length
        record files.  For receiving, this option packs
        characters into fixed-length records regardless of
        newline characters.  For sending, full records with no
        record separator are sent. Setting RAW ON sets EXPAND-
        TABS OFF.  To receive RAW and expand tabs, EXPAND-TABS ON
        must be entered after setting RAW ON.

             <value> = ON:  Received records are filled character
             by character. A new record is started only when the
             current record is full. Transmitted records have no
             record separator.

             <value> = OFF: This is the default. Records received
             are filled character-by-character. A new record is
             started each time a  newline character is received.
             Records sent are separated by CR, LF.

        RECORD-SIZE <d>:  Sets the record length in terms of
        UNITS for the received file to <d>.  Default RECORD-SIZE
        is 15.

        UNITS <type>:  Sets the unit used to measure RECORD-SIZE
        and BLOCKSIZE attributes for a file being received.

             <type> = CHARACTERS:  Units are eight-bit bytes.

             <type> = WORDS:  Units are A-series system words, 48-
             bits/word (6 characters/word).  This is the default.

SET INCOMPLETE <disposition>

        When a file transfer cannot be completed (for instance,
        because the communication path suddenly breaks or becomes
        too noisy), the Kermit receiving the file can either
        discard or retain the incomplete portion of the file that
        has been received.

        <disposition> = DISCARD: Remove the partially received
        file from the A-Series disk.

        <disposition> = KEEP:  Retain the file on disk containing
        all the data transferred successfully up until the error
        occurred. This option may be useful when transferring
        very long files, if it is possible for the sending system
        start again at the place it was interrupted, e.g. by
        breaking the end of the file off with a text editor.
        This is the default.


SET RETRY <parameter> <value>

        Set the maximum number of times AS-Kermit will retry an
        operation before giving up and terminating the transfer.
        Possible <parameter> values are INITIAL-CONNECTION and
        PACKETS.  The default <value> settings are 20 and 10,
        respectively, but these can be set higher when the
        connection is noisy, or when other problems prevent a
        transfer from completing successfully.

SET RECEIVE <parameter>
SET SEND <parameter>

        ACTUAL-FILETITLE <value>: Controls conversion of file
        names to/from A-series format.

             <value> = ON:  Do not perform file name conversion.
             Use the file name received for the title,  or send the
             unaltered file title as the file name.

             <value> = OFF:  This is the default.  Perform file
             name conversion. Change file names to be usable by the
             receiving system.

        END-OF-LINE <d>:  Specify the character with which the
        remote Kermit should terminate its packets.  Carriage
        Return (ASCII 15) is the default.  AS-Kermit requires the
        packet terminator for packets it receives to be a
        carriage return. <d> is the decimal value of the ASCII
        character.

        PACKET-LENGTH <d>:  Specify the longest packet the remote
        Kermit may send.  Legal values of <d> are 10 to 2000; the
        default is 94 (88 data bytes plus 6 packet bytes).

        PADCHAR <d>:  Specify a padding character to precede
        packets.  Not needed for packets received by AS-Kermit.

        PADDING <d>:  Specify the number of padding characters to
        be inserted before packets.   Not needed for packets
        received by AS-Kermit.

        PAUSE <d>:  When receiving a file, pause the specified
        number of tenths of a second between receiving a packet
        and sending the acknowledgement (ACK) or the resend (NAK)
        reply.   Default is no pause, <d> = 0.

        QUOTE <char>:  Specify the character the remote Kermit
        should use for quoting control characters.  The default
        is "#" and there is generally no reason to change this.
        Permissible values are "!"  to "~" , i.e., the ASCII
        characters in the printable range.  <char> is an actual
        character.

        START-OF-PACKET <d>:  Specify the character the remote
        Kermit is using to start its packets, normally ASCII 1
        (SOH).  If the remote Kermit is incapable of transmitting
        an ASCII 1, this command informs AS-Kermit what character
        to expect.  Permissible values are 1 (SOH) to 31 (US).
        <d> is the decimal value of the character.

        TIMEOUT <d>:  The number of seconds AS-Kermit waits after
        sending a packet for an acknowledgement from the remote
        Kermit. The delay may be adjusted to accommodate various
        line speeds, or to compensate for slow systems.  Legal
        values for <d> range from 1 to 94 seconds.  The default
        is 5 seconds.

SHOW <parameter>
STATUS <parameter>

        These two commands are synonyms that show the settings of
        SET command parameters, as well as information about SEND
        or RECEIVE parameters.  The <parameter> is either SEND or
        RECEIVE, and determines which set of information is
        displayed.  The default, if no <parameter> is given, is
        RECEIVE.

TAKE <filespec>

        Read Kermit control commands from a disk file. A "take"
        file contains Kermit commands, one command per record, in
        the same format as those entered from the keyboard.  A
        "take" file should be type data to avoid the possibility
        of a sequence number being interpreted as part of a
        command.  Nested "takes" are not permitted. Each record
        read is echoed to the screen prefixed by "TAKEN: ".  If
        an error occurs, no special action occurs; the next
        command is read and processed, just as if it had come
        from the keyboard.  At startup, AS-Kermit looks for a
        file called KERMITINI and if present, it is processed as
        a TAKE file. KERMITINI is useful for changing default
        Kermit attributes every time AS-Kermit runs.


ASCII to EBCDIC and EBCDIC to ASCII
Translations used by AS-Kermit
Page 1 of 2

 |  A-> E       |  A-> E       |  A-> E       |  A-> E        |
 |  E-----> A   |  E-----> A   |  E-----> A   |  E-----> A    |
 |              |              |              |               |
 |  00  00  00  |  40  7C  20  |  80  20  C3  |  C0  76  7B   |
 |  01  01  01  |  41  C1  A0  |  81  21  61  |  C1  77  41   |
 |  02  02  02  |  42  C2  A1  |  82  22  62  |  C2  78  42   |
 |  03  03  03  |  43  C3  A2  |  83  23  63  |  C3  80  43   |
 |  04  37  9C  |  44  C4  A3  |  84  24  64  |  C4  8A  44   |
 |  05  2D  09  |  45  C5  A4  |  85  15  65  |  C5  8B  45   |
 |  06  2E  86  |  46  C6  A5  |  86  06  66  |  C6  8C  46   |
 |  07  2F  7F  |  47  C7  A6  |  87  17  67  |  C7  8D  47   |
 |  08  16  97  |  48  C8  A7  |  88  28  68  |  C8  8E  48   |
 |  09  05  8D  |  49  C9  A8  |  89  29  69  |  C9  8F  49   |
 |  0A  25  8E  |  4A  D1  5B  |  8A  2A  C4  |  CA  90  E8   |
 |  0B  0B  0B  |  4B  D2  2E  |  8B  2B  C5  |  CB  9A  E9   |
 |  0C  0C  0C  |  4C  D3  3C  |  8C  2C  C6  |  CC  9B  EA   |
 |  0D  0D  0D  |  4D  D4  28  |  8D  09  C7  |  CD  9C  EB   |
 |  0E  0E  0E  |  4E  D5  2B  |  8E  0A  C8  |  CE  9D  EC   |
 |  0F  0F  0F  |  4F  D6  21  |  8F  1B  C9  |  CF  9E  ED   |
 |  10  10  10  |  50  D7  26  |  90  30  CA  |  D0  9F  7D   |
 |  11  11  11  |  51  D8  A9  |  91  31  6A  |  D1  A0  4A   |
 |  12  12  12  |  52  D9  AA  |  92  1A  6B  |  D2  AA  4B   |
 |  13  13  13  |  53  E2  AB  |  93  33  6C  |  D3  AB  4C   |
 |  14  3C  9D  |  54  E3  AC  |  94  34  6D  |  D4  AC  4D   |
 |  15  3D  85  |  55  E4  AD  |  95  35  6E  |  D5  AD  4E   |
 |  16  32  08  |  56  E5  AE  |  96  36  6F  |  D6  AE  4F   |
 |  17  26  87  |  57  E6  AF  |  97  08  70  |  D7  AF  50   |
 |  18  18  18  |  58  E7  B0  |  98  38  71  |  D8  B0  51   |
 |  19  19  19  |  59  E8  B1  |  99  39  72  |  D9  B1  52   |
 |  1A  3F  92  |  5A  E9  5D  |  9A  3A  CB  |  DA  B2  EE   |
 |  1B  27  8F  |  5B  4A  24  |  9B  3B  CC  |  DB  B3  EF   |
 |  1C  1C  1C  |  5C  E0  2A  |  9C  04  CD  |  DC  B4  F0   |
 |  1D  1D  1D  |  5D  5A  29  |  9D  14  CE  |  DD  B5  F1   |
 |  1E  1E  1E  |  5E  5F  3B  |  9E  3E  CF  |  DE  B6  F2   |
 |  1F  1F  1F  |  5F  6D  5E  |  9F  E1  D0  |  DF  B7  F3   |
 |  20  40  80  |  60  79  2D  |  A0  41  D1  |  E0  B8  5C   |
 |  21  4F  81  |  61  81  2F  |  A1  42  7E  |  E1  B9  9F   |
 |  22  7F  82  |  62  82  B2  |  A2  43  73  |  E2  BA  53   |
 |  23  7B  83  |  63  83  B3  |  A3  44  74  |  E3  BB  54   |
 |  24  5B  84  |  64  84  B4  |  A4  45  75  |  E4  BC  55   |
 |  25  6C  0A  |  65  85  B5  |  A5  46  76  |  E5  BD  56   |
 |  26  50  17  |  66  86  B6  |  A6  47  77  |  E6  BE  57   |
 |  27  7D  1B  |  67  87  B7  |  A7  48  78  |  E7  BF  58   |
 |  28  4D  88  |  68  88  B8  |  A8  49  79  |  E8  CA  59   |
 |  29  5D  89  |  69  89  B9  |  A9  51  7A  |  E9  CB  5A   |
 |  2A  5C  8A  |  6A  91  7C  |  AA  52  D2  |  EA  CC  F4   |
 |  2B  4E  8B  |  6B  92  2C  |  AB  53  D3  |  EB  CD  F5   |
 |  2C  6B  8C  |  6C  93  25  |  AC  54  D4  |  EC  CE  F6   |
 |  2D  60  05  |  6D  94  5F  |  AD  55  D5  |  ED  CF  F7   |
 |  2E  4B  06  |  6E  95  3E  |  AE  56  D6  |  EE  DA  F8   |
 |  2F  61  07  |  6F  96  3F  |  AF  57  D7  |  EF  DB  F9   |





ASCII to EBCDIC and EBCDIC to ASCII
Translations used by AS-Kermit
Page 2 of 2


 |  A-> E        |  A-> E        |  A-> E        |  A-> E        |
 |  E-----> A    |  E-----> A    |  E-----> A    |  E-----> A    |
 |               |               |               |               |
 |  30  F0  90   |  70  97  BA   |  B0  58  D8   |  F0  DC  30   |
 |  31  F1  91   |  71  98  BB   |  B1  59  D9   |  F1  DD  31   |
 |  32  F2  16   |  72  99  BC   |  B2  62  DA   |  F2  DE  32   |
 |  33  F3  93   |  73  A2  BD   |  B3  63  DB   |  F3  DF  33   |
 |  34  F4  94   |  74  A3  BE   |  B4  64  DC   |  F4  EA  34   |
 |  35  F5  95   |  75  A4  BF   |  B5  65  DD   |  F5  EB  35   |
 |  36  F6  96   |  76  A5  C0   |  B6  66  DE   |  F6  EC  36   |
 |  37  F7  04   |  77  A6  C1   |  B7  67  DF   |  F7  ED  37   |
 |  38  F8  98   |  78  A7  C2   |  B8  68  E0   |  F8  EE  38   |
 |  39  F9  99   |  79  A8  60   |  B9  69  E1   |  F9  EF  39   |
 |  3A  7A  9A   |  7A  A9  3A   |  BA  70  E2   |  FA  FA  FA   |
 |  3B  5E  9B   |  7B  C0  23   |  BB  71  E3   |  FB  FB  FB   |
 |  3C  4C  14   |  7C  6A  40   |  BC  72  E4   |  FC  FC  FC   |
 |  3D  7E  15   |  7D  D0  27   |  BD  73  E5   |  FD  FD  FD   |
 |  3E  6E  9E   |  7E  A1  3D   |  BE  74  E6   |  FE  FE  FE   |
 |  3F  6F  1A   |  7F  07  22   |  BF  75  E7   |  FF  FF  FF   |